## Slide 1
Sequencer Debugger
Low-level at your fingerprints
Project number: 22-1-2-2659
Student: Dor Golfaiz
ID: 316060805
Mentor: Michal Carmeli
Mentor’s Signature: Michal

## Slide 2: The Project
The Project

## Slide 3: What are we debugging?
The Project
What is the Sequencer?
  A controller in the chip whose purpose is to control a basic flow of measurement: scanning over bands, transmitting, turning on/off modules at specific times, etc.
  Its purpose is to release the external CPU from real-time operations and release the real-time requirements from the external CPU. (e.g., 4 minutes vs 100 ms)
  9 instructions, ALU, Peripherals (Condition, Counters). Data Width (word): 2 bytes. Program Memory Size – 32K instructions (128 KB) Parameters Memory Size – 16K parameters (32 KB)
Sequencer Code
( 0101101… )
Recording Program
(DB + XML)
Compiled to…

## Slide 4
The Project
Main issues to remember:
A question to think about …
Assuming we can generate a “breakpoint” code (some kind of a conditional wait)
How can we insert real-time breakpoints into a compiled code?
Don’t worry, we will answer it soon 
Sequencer Code
( 0101101… )
Recording Program
(DB + XML)
Compiled to…

## Slide 5
System Requirements

## Slide 6: A Debugger Software Architecture
GUI
(Front)
Debugger
(Back)
Adapter

## Slide 7: A Debugger Software Architecture
GUI
(Front)
VS Code for
“ VS Code allows you to easily integrate existing debuggers into VS Code, while having a common user interface with all of them ”
which means you can enjoy VS Code as our debugger GUI just by implementing the debug adapter which will connect the debugger to VS Code.
If you think about it, all the debuggers are the same…

## Slide 8: A Debugger Software Architecture
GUI
(Front)
Debugger
(Back)
Adapter

## Slide 9: A Debugger Software Architecture
Debugger
(Back)
Supported features by the debugger
Breakpoint functionality (incl. stepping)
Call stack
Local Variables (Read + Write)
Watchers (Read + Write)
Optional – Conditional Breakpoints,

## Slide 10: A Debugger Software Architecture
Lets say we have a breakpoint functionality,
How can we implement the following?
Stepping ?
Step In ?
Step Out ?
Debugger
(Back)

## Slide 11: Block Diagram
Block Diagram

## Slide 12: Block Diagram
Running the program Breakpoint Requests
Stopping on breakpoint
Debugger Breakpoint Implementation
Continue / Step
Running the program Breakpoint Requests
Stopping on breakpoint
Debugger Breakpoint Implementation
Continue / Step

## Slide 13: Block Diagram
Running the program Breakpoint Requests
Jump to BreakPoint Block
BreakPoint Block
Debugger Breakpoint Implementation
Stopping on breakpoint
Continue / Step

## Slide 14: Product
So, what do we have so far?

## Slide 15: Product
Breakpoint Loop
  A series of opcodes, designed to keep the sequencer in a conditional wait
  Was able to release the conditional wait by writing to a specific register
DAP - Command Processor module
  Translates a DAP request to a function call that handles a given request
  Logs handled requests and current status
  Returns a response to DAP, letting VSCode know whether the handling was successful or failed.
Debugger API
  Implements the functions called by Command Processor
  Returns information needed for VSCode’s response.

## Slide 16: Updated Schedule
Updated Schedule

## Slide 17: Updated Schedule
אבן דרך | פירוט | תאריך יעד | הערות
המשך Command Processor | מימוש סופי של ה-Adapter, המכיל את ארגז הכלים הרצוי, והעברת כל פעולה שהתבצעה בו פקודה לדיבאגר, כך שהאבסטרקציה תושלם והדיבאגר יוכל להתחבר ל-GUI במאמץ מינימלי, וכל שעליו לעשות הוא לממש את האבסטרקציות הנ"ל על המעבד | 10.3.23 | 
פיתוח Debugger | מימוש האבסטרקציות שפורטו לעיל – הכנסת Breakpoint, כתיבה לרגיסטרים, שמירת Call Stack אך כל זה ישירות על המעבד בעזרת צריבת אופקודים בזמן ריצה ישירות ל-IRAM. | 30.4.23 | 
ניתוח התוצאות | השוואה וניתוח התוצאות לצד המטרות שהצגתי בתחילת העבודה על הפרויקט | 4.5.23 | 
הרחבת הכלי | פיתוח והרחבת ה-Debugger בעזרת כלל ההצעות שהועלו במסמך זה- Syntax Highlighting, code navigation, etc.. | 20.5.23 | 
הגשת פוסטר וסיום העבודה בפרויקט |  | 28.5.23 | 
המשך - הרחבת הכלי | פיתוח והרחבת ה-Debugger בעזרת כלל ההצעות שהועלו במסמך זה- Syntax Highlighting, code navigation, etc.. | 20.6.23 | 
הגשת ספר הפרויקט + מצגת הסיום |  | 29.6.23 | 

## Slide 18: Updated Schedule
Reasons for changes in the schedule
  GUI Development – Instead of developing a GUI, I presented a way to use VSCode’s well-known and easy-to-use debugging flow, while debugging sequencer code – using DAP. So GUI implementation is off the table.
  Testing the debugger – The stage of testing the debugger was removed, since instead of testing on some sequencer code that does nothing, I decided to test it on real operational Vayyar Sequencer Code, and I can check that I stopped in a breakpoint using a scope.
  The biggest part of the new scheduled work plan is to implement the debugger – making it work for every case, for example stepping at the end of a function, stepping out of functions, adding watchers, etc. That is the crucial part.

## Slide 19
Vayyar Imaging Confidential
Thank You